## Slide 1: Ground-based remote sensing of clouds

## Slide 2: Ground-based cloud profiling
Notes: Developer (database design and administration
- web development (full stack)
- development languages: mostly Java (with Spring-boot) and Javascript (VueJS), but also Python and PHP )

## Slide 3: Evaluation of cloud microphysics in NWP and climate models using radar and lidar
Example of using cloud radar data to understand and improve NWP
  Ice sublimation rate
Why do we need to combine radar and lidar?
  Both are active instruments, but are sensitive to different moments of the size distribution
    complementary
  Vertical measurements for long-term microphysical studies
    terminal velocity -> size
Formal framework for comparing models and observations
  Introduce Cloudnet (now with ACTRIS)
    Compare parameter of your choice
    Provide skill scores (how good is your forecast!)

## Slide 4: Ice sublimation rate
Study the cooling due to evaporation of hydrometeors
Dynamical impact of ice/snow potentially more important than rain due to high evaporation rate within a shallow layer
Relatively low fall velocity
Lower bulk density
Cooling rates of a few K m-1 hr-1
enhance slantwise convection
initiate vertical convection

## Slide 5: Ice sublimation rate
Sublimation zone: gradient in IWC (calculated from Z)
Clear signature in:
Doppler velocity
Spectral width
Zone is also highly turbulent

## Slide 6: Ice sublimation rate
Reasons for discrepancy
Vertical resolution?
Ice microphysics?
Relative humidity?

## Slide 7: Ice sublimation rate
1D model initialised with radiosonde profile of T, p, q
  Similar sublimation depth to observed
  Therefore, model microphysics correct
NWP model has same microphysics
  Sublimation zone still too deep
  Attributed to errors in RH

## Slide 8: Ground-based cloud profiling
Notes: Developer (database design and administration
- web development (full stack)
- development languages: mostly Java (with Spring-boot) and Javascript (VueJS), but also Python and PHP )

## Slide 9: Ground-based remote sensing of clouds
Radar: Z~D6
Sensitive to large particles (ice, drizzle)
Lidar: β~D2
Sensitive to small particles (droplets, aerosol)
Detects cloud base
Penetrates ice cloud
Strong echo from liquid clouds
Detects cloud top

## Slide 10: Terminal Fall Velocity (Beard et al., 1976)
For water spheres
Fall speed varies slightly with pressure and temperature
Aerosol: r~5e-7 m
Cloud: r~5e-6 m
Ice : r~2e-4 m

## Slide 11
Notes: Front passing over a vertically pointing radar and lidar
Showers produce negative Doppler velocity. Altocumulus and cirrus are not falling
Fog contains small water droplets, these attenuate the lidar so can’t ‘see’ altocumulus and cirrus
Lidar identifies stratocumulus better than radar because it has smaller particles

## Slide 12
Notes: Low level stratocumulus and drizzle
Not detected small droplets
Layer at 500m enhanced backscatter

## Slide 13: Ground-based cloud profiling
Notes: Developer (database design and administration
- web development (full stack)
- development languages: mostly Java (with Spring-boot) and Javascript (VueJS), but also Python and PHP )

## Slide 14
Original aim: to retrieve and evaluate the crucial cloud variables in forecast and climate models
  8+ models: global, mesoscale and high-resolution forecast models
  Variables: cloud fraction, LWC, IWC, plus a number of others
  Sites: 10+ across Europe plus worldwide ARM sites
  Period: several years to avoid unrepresentative case studies
Current status: characterise cloud properties
  Funded by ACTRIS ERIC to apply to European sites

## Slide 15
Level 1b
Minimum instrument requirements at each site
  Cloud radar, lidar, microwave radiometer, rain gauge, model or sondes
Radar
Lidar

## Slide 16: Level 1c
Ice
Liquid
Rain
Aerosol
Instrument Synergy product
  Example of target classification and data quality fields:

## Slide 17: Level 2a
Ice water content (+errors) on observational grid
  IWC from Z and temperature (Hogan et al. JAMC 2006)
Note larger error above melting-layer due to uncertain attenuation
IWC not reported if rain at ground

## Slide 18: Level 2a
Liquid water content (+errors) on observational grid
  “Scaled adiabatic” method (LWP +T + liquid cloud boundaries)
Reflectivity contains sporadic drizzle: not well related to LWC
LWC assumed constant or increasing with height has little effect on statistics

## Slide 19: Level 2b
Variables on model grid
  Averaged horizontally and vertically to grid of each model

## Slide 22
Level 2a/2b
Cloud products on (L2a) observational and (L2b) model grid
  Water content and cloud fraction
L2a IWC on radar/lidar grid
L2b Cloud fraction on model grid

## Slide 23
Chilbolton
Observations
Met Office
Mesoscale Model
ECMWF
Global Model
Meteo-France
ARPEGE Model
KNMI
RACMO Model
Swedish RCA model
Cloud fraction

## Slide 24
NCEP GFS 2007
  NCEP GFS shows good agreement for Amount-When-Present
  Problem is how often cloud is forecast
Cloud fraction at SGP

## Slide 25
Cloud fraction in 7 models

## Slide 26
A change to Meteo-France cloud scheme

## Slide 27: Composites: ECMWF, Lindenberg
Observation Model
Cloud fraction

## Slide 28: Composites: ECMWF, Lindenberg
Observation Model
Cloud fraction
Ice water content

## Slide 29: Composites: ECMWF, Lindenberg
Observation Model
Cloud fraction
Ice water content
Liquid water content

## Slide 30: Composites: ECMWF, Lindenberg
Observation Model
Cloud fraction
Skill score SEDI

## Slide 31
Diurnal composite of cloud fraction in summer
Mace Head
Chilbolton
Potenza
Lindenberg
Leipzig
Sodankylä
Juelich
Notes: Provide a concise overview of the work done (technical review) since the beginning of the project until June 2013 with comparison to the original description of work in Annex I.
The progress of work should be summarized with respect to the content of the work (e.g., tasks) and not with respect to the deliverables.
In case of deviations from the original work plan please explain the reasons (incl. corrective actions).

## Slide 32
Diurnal composite of cloud fraction in summer
Mace Head
Chilbolton
Potenza
Lindenberg
Sodankylä
Juelich
Marine
Continental
Marine to Continental transition:
Less cloud
Enhanced daytime convection
Notes: Provide a concise overview of the work done (technical review) since the beginning of the project until June 2013 with comparison to the original description of work in Annex I.
The progress of work should be summarized with respect to the content of the work (e.g., tasks) and not with respect to the deliverables.
In case of deviations from the original work plan please explain the reasons (incl. corrective actions).

## Slide 33: Decade of NWP forecast skill at Lindenberg

## Slide 34
Model spin up
Assimilation preferred state
Forecast Lead-time

## Slide 35: Forecast Lead-time
Model spin up
Assimilation preferred state
Model preferred state

## Slide 36
Decade of forecast skill at SGP 2001-2010

## Slide 37: Focus on Harmonie
3 stations in HARMONIE-AROME MetCoop domain:
Norunda, Sweden
Hyytiälä, Finland
Lindenberg, Germany
Observations
Model

## Slide 38
First identify if model has clouds in the right place at the right time:
use several months of observation and model data
compare cloud fraction
Then evaluate microphysics
Observations: all solid precipitation treated as ice – no separation into ice classes (e.g. snow, graupel)
Observation-model comparison – cloud fraction at Norunda
Cloud fraction
If include model snow and graupel as cloud -> better agreement with observations

## Slide 39
Observation-model comparison – ice water content – at Norunda
Mean ice water content also compares quite well at all levels, if snow and graupel included.

## Slide 40
Observation-model comparison – ice water content – at Norunda
Mean ice water content also compares quite well at all levels, if snow and graupel included.
Might get the mean amount right but for the wrong reason. Can also calculate
frequency of occurence (how often do ice clouds occur),
and amount when present (what ice water contents do these clouds have)

## Slide 41
Observation-model comparison – ice water content – at Norunda
Frequency of occurrence of ice above a low threshold amount too high once snow/graupel included
Not enough ice water content in mid level clouds
Close to surface: ice water content too high
Frequency of occurrence
Amount when present
Mean amount

## Slide 42
Observation-model comparison – ice water content close to surface
Close to surface: ice water content too high
Robust signal at all stations – implication for model microphysics
Too much ice in graupel phase? Less time to sublime while falling?
Norunda
Hyytiälä
Lindenberg

## Slide 43: CLU: cloud profiling data portal
Characterisation and
processes
Satellite Cal Val
Model evaluation
Juelich
https://cloudnet.fmi.fi

## Slide 44: ACTRIS cloud profiling
Vertical winds and turbulent properties:
Boundary layer and in-cloud (Radar and Doppler lidar)
Weak turbulence:
Cirrus
Strong turbulence
Evaporating ice
Stratocumulus
Boundary layer
dynamics
Identify vertical mixing and diagnose source
Evaluate satellite retrievals (e.g. cloud top height)
Multiple hydrometeor modes, phases in same volume
Cloud microphysics: Doppler spectra, surface disdrometer
Size distributions, mass-density, particle shape

## Slide 46
Pilot for international stakeholders
Bucharest
Granada
Hyytiälä
Kenttärova
Juelich
Cabauw
Chilbolton
Galati
Lindenberg
Mindelo
Neumayer
Ny Ålesund
Palaiseau
Cloud
fraction
EARTHCARE Cal/Val

## Slide 47: Ground-based cloud profiling
Notes: Developer (database design and administration
- web development (full stack)
- development languages: mostly Java (with Spring-boot) and Javascript (VueJS), but also Python and PHP )

## Slide 50
height
Boundary layer
Seasonal composite:
Juelich

## Slide 52: Outlook
Multiple metrics for evaluating clouds in models
  Cloudnet is implementing an evaluation interface
Large number of cloud profiling stations in Europe
  5+ stations with >10 years of data
ACTRIS is funded for the long term
  Opportunities for operational and project-based support

## Slide 54: Level 2a
Liquid water content (+errors) on observational grid
  “Scaled adiabatic” method (LWP +T + liquid cloud boundaries)
Reflectivity contains sporadic drizzle: not well related to LWC
LWC assumed constant or increasing with height has little effect on statistics

## Slide 55
Method of Albrecht et al. (1990), Boers et al. (2000)
  Use lidar/radar to determine cloud boundaries
  Assume linear increase of LWC with height
  Scale LWC profile to match LWP from radiometers
LWC
Height
Cloud base
(lidar)
Cloud top
(radar)
Model
levels
Liquid water content

## Slide 56
  LWC not retrieved in rain
Liquid water content

## Slide 57
Liquid water content

## Slide 58
Liquid water content

## Slide 59
Liquid water content

## Slide 60: Level 2a
Cloud products on observational grid
  Includes both simple and complicated algorithms
  Radar-lidar IWC (Donovan et al. 2000) is accurate but only works in the 10% of ice clouds detected by lidar
  IWC from Z and T (Hogan et al. 2006) works almost all the time; comparison to radar-lidar method shows appreciable random error but low bias: use this to evaluate models

## Slide 61: Level 2a
Ice water content (+errors) on observational grid
  IWC from Z and temperature (Hogan et al., JAMC, 2006)
Note larger error above melting-layer due to uncertain attenuation
IWC not reported if rain at ground

## Slide 62: Ice water content
Method of Hogan et al. (2006)
Using coordinated aircraft data (EUCREX) and 3 GHz scans
Fit to Z and
temperature
35 GHz

## Slide 63
Method of Hogan et al. (2006)
Using coordinated aircraft data (EUCREX) and 3 GHz scans
Fit to Z and
temperature
94 GHz
Ice water content

## Slide 64
Ice water content

## Slide 65
Ice water content

## Slide 66: Level 2b
Variables on model grid
  Averaged horizontally and vertically to grid of each model

## Slide 67: Drizzle below cloud
  Doppler radar and lidar - 4 observables (O’Connor et al. 2005)
    Radar/lidar ratio provides information on particle size

## Slide 68: Drizzle below cloud
  Doppler radar and lidar - 4 observables (O’Connor et al. 2005)
    Radar/lidar ratio provides information on particle size
  Retrieve three components of drizzle DSD (N, D, μ).
    Can then calculate LWC, LWF and vertical air velocity, w.

## Slide 69
  Doppler radar and lidar - 4 observables (O’Connor et al. 2005)
    Radar/lidar ratio provides information on particle size
Drizzle below cloud

## Slide 71
Truly equitable
Asymptotically equitable
Not equitable
Properties of various measures